## Slide 1: Fluid Flow
Paul Drosinis
UBC Phys 420

## Slide 2: Introduction
Short history on fluid dynamics
Why bother studying fluid flow?
Difference between Newtonian and Non-Newtonian Fluids
Laminar vs. Turbulent Flow and the Navier-Stokes Equation
Reynolds Number

## Slide 3: Brief History
Archimedes (285-212 B.C.) – formulated law of buoyancy and applied it to floating and submerged bodies
ischoolsfndiloy.wordpress.com

## Slide 4: Brief History
Isaac Newton (1642-1727) – postulated laws of motion and law of viscosity of linear fluids
Frictionless fluids – many problems solved by great mathematicians (Euler, Lagrange, Laplace, Bernoulli etc.)
http://psychogeeks.com/isaac-newton/

## Slide 5: Brief History
Osborne Reynolds (1842-1912) – classic pipe experiment illustrating importance of so-called ‘Reynolds Number’
http://en.academic.ru/dic.nsf/enwiki/191600

## Slide 6: Why Study Fluid Flow?
Widely applicable to many phenomena: blood flow through arteries/veins, automotive design, aeronautics
Deeper understanding can be used to design faster and more efficient ships/airplanes

## Slide 7: Stress and Shear
Stress: defined as force per unit area
-has magnitude and direction
Can have both normal and tangential stresses
http://www.scribd.com/doc/10119418/Fluid-Mechanics-Lecture-Notes-I

## Slide 8: Finding Newton’s Law of Viscosity
We are going to model a ‘block of fluid’ as many sheets stacked on top of one another
In this way we can figure out how the shear force is related to the viscosity

## Slide 9: What is viscosity?
Property of a fluid that describes its ability to resist flow
It’s a measure of the internal friction associated with this flow
Substance | Viscosity(kg/m*s)
Air | 0.02
Water | 1.00
Milk | 1.13
Blood | 4
Olive Oil | 90
Motor Oil | 320

## Slide 10: Stress and Shear
Force in a fluid acts along the surface of each sheet and is proportional to the relative velocity
http://www.britannica.com/EBchecked/topic/211272/fluid-mechanics

## Slide 11: Finding Shear Force
y
x

## Slide 12: Finding Shear Force
Forces act parallel to the sheets
If we talk about force per unit area, find that:
As ℇ gets smaller, the difference becomes a gradient

## Slide 13: Shear Stress
If we model a body of fluid as composed of many thin sheets, find that:
Stress
Viscosity
Velocity
Gradient

## Slide 14: Finding Shear Force
Constant of proportionality here is the viscosity: η
What are its units?

## Slide 15: Units of Viscosity

## Slide 16: Newtonian vs. Non Newtonian Fluid
Linear dependence of shear stress with velocity gradient: Newton’s Law of Viscosity
Viscosity will change only if temperature or pressure changes
Don’t resist much when a force is applied
Ex: water

## Slide 17: Newtonian vs. Non Newtonian Fluid
Non-Newtonian fluids will change viscosity when a force is applied
Can cause them to become thicker or thinner depending on the substance in question

## Slide 18: DEMO!

## Slide 19: Navier-Stokes Equation
Set of non-linear partial differential equations that describe fluid flow
Also used to model weather patterns, ocean currents, and airflow around objects
Very difficult equation to solve

## Slide 20: Navier-Stokes Equation
Pressure Gradient
Viscous
Term
Body
Forces
Rate Change in
Momentum Density

## Slide 21: Reynolds Number
Ratio of inertial forces to viscous forces in a fluid
Describes the relative importance of each term
Important factor in determining the transition from laminar to turbulent flow

## Slide 22: Reynolds Number
Can be calculated from the Navier-Stokes equation
More intuitively:

## Slide 23: Reynolds Number
η - viscosity
ρ – density
u - velocity
d – characteristic length

## Slide 24: Reynolds Number Units?
Reynolds number is dimensionless!

## Slide 25: Laminar Flow
Fluid travels smoothly in similar paths
No mixing between adjacent ‘sheets’ of fluid
Sheets slide over one another
All flow properties constant at any given point (velocity, pressure, etc.)

## Slide 26: Laminar Flow
https://wiki.brown.edu/confluence/display/PhysicsLabs/PHYS+0050+and+0070+Handouts

## Slide 27: Turbulent Flow
Formation of eddies and vortices associated with high Reynolds number fluids
Flow becomes chaotic
Complete description of turbulent flow still an unsolved problem of physics

## Slide 28: Turbulent Flow
http://www.colorado.edu/MCEN/flowvis/gallerie/2010/Team-1/FV_popup1-8.htm

## Slide 29: Laminar vs. Turbulent Flow
Fluids behave very differently depending on the value of the Reynolds number
Low Re – Laminar Flow
High Re – Turbulent Flow

## Slide 30: Questions?